## Slide 1
Digital Receivers for Radio Astronomy
Paul Roberts
CSIRO Astronomy and Space Science
Engineering Development Group

## Slide 2: Plan
Digital receiver
- definition
- differences between analogue receivers and types of digital receivers
Pro and cons of using a fully digital receiver.
Currently used digital receivers
- eg ASKAP Design Enhancements
SKA digital receivers
- specs
- current implementation options
Summary and suggestions for the immediate future

## Slide 3: Digital Receivers
Digital receiver
Digitise input RF band without prior down-conversion and analogue processing
Performs all signal processing operations in the digital domain (software defined radio)
Dividing line between firmware/software flexible

## Slide 4: Conventional Receivers
ADC
LO1
LO2
LNA
ANT
Typical Analogue Receiver
Sample
clock
Digital
Spectrum

## Slide 5: Digital Receivers
ADC
LNA
ANT
Digital Receiver with direct/bandpass sampling
Gain
Digital
Spectrum

## Slide 6: Digital Receivers
ADC
LNA
ANT
Fully digital receiver
Full Band Filter
Gain
Digital
Spectrum

## Slide 7: Digital Receivers
Advantages of fully digital receivers over analogue
- flexibility
- simplification
- integration
- production
- cost

## Slide 8: Digital Receivers
Flexibility
Adaptable signal processing – research instrument
All information present – allows innovative signal processing
- adaptive RFI filter etc
- programmable dedispersions etc
- a particular example real-time time-domain RFI excision

## Slide 9: Parkes 21cm Multibeam Experiment
Centaurus A neutrinos
RFI
Veto

## Slide 10: Parkes: RFI pulse
Pol A
Pol B
4 micro sec
4 micro sec

## Slide 11: Digital Receivers
Simplification
Numerous analogue components replaced with a few (complex) digital components
Analogue parts difficult to tune/match.
A single LO (the sample clock)
Integration
Lowering complexity key to building large systems affordably and efficiently
Critical for large number of signal paths – PAFS
Reduces power consumption – ongoing costs/cooling
and weight (ideally near focus)

## Slide 12: Digital Receivers
Production
Analogue systems time consuming/complicated to test
Digital systems can take advantage of well developed test protocols like BSCAN and other digital self-test
Cost
Rides on the back of high-volume semiconductor fabrication technology – potential for low cost if sufficient volume
CMOS RF devices designed with a measure-and-calibrate approach. Allows standard cmos process to be used
e.g ASKAP ADCs about 1/10 of cost of prev generation
- Implications for SKA receiver system design

## Slide 13: Digital Receivers
Challenges of fully digital receivers
- stability
- present cost in small volume
- self generated interference
- performance
Stability - high gain at a single frequency from ADC to LNA
- wider bandwidth helps
Interference - RF and digital co-located in a small volume. Optimal
implementation has receiver near focus.
Cost - currently at the low volume/prototyping point
- custom IC devices expensive if not sufficient volume
Performance
- out-of-band interference etc.

## Slide 14: ASKAP’s Design Enhancement simplification
ADC
ADC

## Slide 15: Digital Receiver for SKA
Canonical SKA –> DC-15 GHz fully digital receiver including
signal processing (band-selection @2GHz, filtering, adaptive RFI control, fringe rotation, delay compensation, – beam forming further down the chain.
Approaches available today:

## Slide 16: Digital Receiver for SKA
Implementation based on available prototype devices
Micram 6-bit, DC-15 GHz, 30 GS/s ADC prototype coupled to Xilinx LX240 FPGA
Current CASS development platform
Small scale production and prototyping solution – high speed interconnects – in and out of chips

## Slide 17: Digital Receiver for SKA
Direct receiver ASIC for SKA?
SKA will require high-integration solutions to be practical for thousands of signal paths (power, cost, complexity) –especially for PAFS
Technology exists now to develop a direct digitisation ASIC with ability to satisfy SKA requirements (100/400 Gbit Optical Transmission Market)
Can incorporate digitisation, signal processing and serial data drivers – RF-to-data

## Slide 18
Notes: 4.4 W for 1800 MHz ASKAP adc’s
65nm CMOS

## Slide 19: ASIC for SKA
Cost of NRE main impediment – too much for one institute but not-unreasonable in SKA context considering savings
Libraries can be accessed at minimal cost
Can produce a virtual design guaranteed to meet timing
Can produce virtual design without committing to expensive layout
Having a synthesised complete design ready for layout would provide leverage when SKA funding decisions are made
Expertise in all areas required

## Slide 20: Summary
Fully digital receivers offer many attractive features for Radio – Astronomy
Technology has recently advanced to the point where this is feasible for SKA

## Slide 21: Thank you
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
CASS Engineering Development Group
Dr. Paul Roberts
Phone: 61 2 9372 4365
Email: paul.roberts@csiro.au
Web: www.csiro.au/org/cass